2TGEU Computer pins

| THW | OT | VF |  | TL | PSW | IDL |  | OX | Vc |  | Vs | E1 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| E02 | E01 | #20 | #10 | THA |  | E1 |  | STA | +B | VB | E2 | IG |

IG			ignition signal

VC, VB, VS		air flow meter

IDL, PSW, TL		throttle body

THA			intake air temperature

THW			coolant temperature

OX,OT			oxygen sensor

#10, #20 		injectors

E1, E2, E01, E02 		grounds

+B			power supply to ECU

STA			starter signal

2TG Engine tightening torque

| Tightening Parts | Kg-m | Ft-lb |
| --- | --- | --- |
| Cylinder head x Cylinder block | 7.2 – 8.8 | 53-63 |
| Intake manifold x Cylinder head | 1.6 – 2.2 | 12-15 |
| Exhaust manifold x Cylinder head | 3.5 – 4.5 | 26-32 |
| Crankshaft bearing cap x Cylinder block | 7.2 – 8.8 | 53-63 |
| Connecting rod cap x connecting rod | 4.0 – 5.0 | 29-36 |
| Crankshaft pulley x crankshaft | 6.0 – 7.0 | 44-50 |
| Flywheel x crankshaft | 8.2 – 8.8 | 60-63 |
| Camshaft sprocket x camshaft | 7.0 – 8.0 | 51-57 |
| Camshaft bearing cap x Cylinder head | 1.2 – 1.8 | 9-13 |
| Distributor drive gear x pump drive shaft | 6.0 – 7.0 | 44-50 |
| Pump drive shaft thrust plate x Cylinder block | 1.5 – 2.1 | 11-15 |
| Chain tensioner No.2 x Cylinder head | 3.0 – 4.0 | 22-28 |
| Chain Vibration damper No.3 x Cylinder head | 1.5 – 2.1 | 11-15 |
| Spark plug x Cylinder head | 1.4 – 2.0 | 11-14 |
| Oil pan x Cylinder block | 0.4 – 0.8 | 3-5 |